Marko Popovic 19323	PONG

Mogla je da se izvrsi optimizacija podelom operatora, ali u svrhu modulranosti projekta, optimizacija nije bila izvrsena. Detektciija kolizije uradjena je na osnovu koordinata strana loptice. Dok je njeno odbijanje vrseno pomocu promene koeficijenta K u zavisnosti od toga da li je naisla na zid, ivicu ekrana ili reket.

entity pong is
    Port ( rst : in STD_LOGIC;
        clk : in STD_LOGIC;
        up : in STD_LOGIC;
        down : in STD_LOGIC;
        VGA_HSYNC : out STD_LOGIC;
        VGA_VSYNC : out STD_LOGIC;
        VGA_RED : out STD_LOGIC;
        VGA_GREEN : out STD_LOGIC;
        VGA_BLUE : out STD_LOGIC
        );
end pong;

architecture Behavioral of pong is
  component VGA_GEN is
    Port ( rst : in STD_LOGIC;
        clk : in STD_LOGIC;
        Rin : in STD_LOGIC;
        Gin : in STD_LOGIC;
        Bin : in STD_LOGIC;

        PxRow : out STD_LOGIC_VECTOR (9 downto 0);
        PxCol : out STD_LOGIC_VECTOR (9 downto 0);
        PxDisp : out STD_LOGIC;
        PxClk : out STD_LOGIC;
        LnClk : out STD_LOGIC;
        FrameSync: out STD_LOGIC;
        VGA_HSYNC : out STD_LOGIC;
        VGA_VSYNC : out STD_LOGIC;
        VGA_RED : out STD_LOGIC;
        VGA_GREEN : out STD_LOGIC;
        VGA_BLUE : out STD_LOGIC);
  end component;
  --pozicije objekata ------------------------------------
  ----ZIIIIIDDDDD--------------------------------------------
  constant wall_x_l: integer :=40;
  constant wall_x_r: integer :=50;
  constant wall_color: std_logic_vector(2 downto 0):="111";
  signal wall_draw:std_logic;
  --REKETTT -------------------------------------------
  --constant paddle_top_y : integer:=360;
 -- constant paddle_bottom_y : integer :=230;
  constant paddle_left_x:integer:=500;
  constant paddle_right_x:integer:=510;
  constant paddle_color: std_logic_vector(2 downto 0):="111";
  signal paddle_draw:std_logic;
  --BALLLLL------------------------------------------
  --constant ball_top_y : integer :=310;
  --constant ball_bottom_y :integer :=300;
 -- constant ball_left_x :integer :=300;
 -- constant ball_right_x: integer :=310;
  constant ball_color: std_logic_vector(2 downto 0):="010";
  signal ball_draw:std_logic;
  ----------------------------singal-------------------------
  signal RGB: std_logic_vector(2 downto 0):="000";
  signal FrameSync: std_logic;
  signal x: integer range 0 to 640;
  signal y :integer range 0 to 480;
  signal PxRow,PxCol : std_logic_vector(9 downto 0);
  ---movement_signals----
 signal paddle_top_y : integer:=300;
 signal paddle_bottom_y : integer :=230;

signal ball_top_y : integer :=240;
signal ball_bottom_y :integer :=230;
signal ball_left_x :integer :=300;
signal ball_right_x: integer :=310;
------------------------
signal dir,paddle_hit,wall_hit,paddle_top,paddle_bottom: std_logic :='0';
signal K: integer:=1;

begin
  vga_sin: VGA_GEN port map (rst=>rst,clk=>clk,
        Rin=>RGB(2),Gin=>RGB(1),Bin=>RGB(0),
        VGA_HSYNC=>VGA_HSYNC,VGA_VSYNC=>VGA_VSYNC,
        VGA_GREEN=>VGA_GREEN,VGA_RED=>VGA_RED,VGA_BLUE=>VGA_BLUE,
        FrameSync=>FrameSync,PxCol=>PxCol,PxRow=>PxRow,
        PxClk=>open,LnClk=>open,PxDisp=>open);
  x<=to_integer(unsigned(pxCol));
  y<=to_integer(unsigned(pxRow));
  -----pokusaj generisanja slika------
  wall_draw<='1' when (x>=wall_x_l and x<=wall_x_r) else '0';
  paddle_draw<='1' when (x>=paddle_left_x and x<=paddle_right_x) and (y>=paddle_bottom_y and y<=paddle_top_y) else '0';
  ball_draw<='1' when (x>=ball_left_x and x<=ball_right_x) and (y>=ball_bottom_y and y<=ball_top_y) else '0';

  RGB<=wall_color when (wall_draw='1' and wall_hit='0') else
       "100" when (wall_draw='1' and wall_hit='1') else
       ball_color when ball_draw='1' else
       paddle_color when paddle_draw='1' else
       "000";
  -----------PADDLE_MOVEMENT------------------
  process(FrameSync)
   begin
    if(rising_edge(FrameSync)) then
      if(up='1' and paddle_bottom_y>=10) then
        paddle_bottom_y<=paddle_bottom_y-3;
        paddle_top_y<=paddle_top_y-3;
      elsif(down='1' and paddle_top_y<=470) then
        paddle_bottom_y<=paddle_bottom_y+3;
        paddle_top_y<=paddle_top_y+3;
      end if;
    end if;
  end process;
----BALL_MOVEMENTS--------------------------
  process(FrameSync)
    begin
      if(rising_edge(FrameSync)) then
        if(ball_top_y<=479 and ball_bottom_y>=5) then
        if(K=1) then
        ball_top_y<=ball_top_y-1;
        ball_bottom_y<=ball_bottom_y-1;
        elsif(K=-1) then
        ball_top_y<=ball_top_y+1;
        ball_bottom_y<=ball_bottom_y+1;
        end if;
      end if;
      if(dir='1') then --needs to go left
        ball_left_x<=ball_left_x-1;
        ball_right_x<=ball_right_x-1;
       else --needs to go right
        ball_left_x<=ball_left_x+1;
        ball_right_x<=ball_right_x+1;
       end if;
      if(paddle_hit='1' or paddle_bottom='1' or paddle_top='1') then --paddle hit ide levo
        dir<='1';
        K<=-K;
       ----------------------------------------------------------
      elsif(wall_hit='1') then --wall hit y=kx+n -- ide desno
        dir<='0';
       ----------------------------------------------------------
      elsif(ball_bottom_y=10) then --bottom screen hit
        K<=-1;
      elsif(ball_top_y=470) then
        K<=+1;
      elsif(ball_right_x>=630) then --respawn
        ball_right_x<=210;
        ball_left_x<=200;
        ball_top_y<=240;
        ball_bottom_y<=230;
        dir<='0';
      end if;
    end if;
  end process;
  --paddle_lenght<=to_unsigned(paddle_top_y - paddle_bottom_y,10);
  paddle_hit<='1' when (ball_right_x=paddle_left_x-1 and (ball_top_y>paddle_bottom_y and ball_bottom_y<paddle_top_y)) else '0';
  wall_hit<='1' when ball_left_x=wall_x_r+1 else '0';
  paddle_top<='1' when (ball_top_y=paddle_bottom_y and ball_right_x>paddle_left_x and ball_right_x<paddle_right_x) else '0';
  paddle_bottom<='1' when (ball_bottom_y=paddle_bottom_y and ball_right_x>paddle_left_x and ball_right_x<paddle_right_x) else '0';

end Behavioral;